## Slide 1: Generating code for the AR Drone 2.0 using Embedded Coder
By Author

## Slide 2: A broad overview: drivers to Simulink and Simulink to AR Drone
Simulink Model
To C code for embedded target
Compile to target (Codesourcery)
C code drivers
MATLAB Legacy code tool
Driver block in Simulink library
Implementing AR Drone 2 driver support in simulink:
Deploying the demo to the AR Drone 2:

## Slide 3: The configuration set
Hardware board: AR_Drone_2_thread.xml
arm_cortex_a8_attri - buteinfo_linux_thread.xml
Add external mode files
Hardware implementation:
Code generation: Toolchain settings :
Set onAfterCodeGen hook
Add target UDP files
Gcc_codesourcery_arm _linux_gnueabihf_gmake _win64_v4.8.mat
Register myfunction.m
Codesourcey toolchain
Download: ssh_download.bat
Assembler / Compiler / Linker
rtwTargetInfo.xml

## Slide 4: The build process
Build Load and Run steps: | Model progression: | Description:
 | Model.slx | Simulink model
Build | Model.rtw | Build Simulink model
Ert.tlc | Model.c files | Build embedded target c code
Posetcodegen: Codesourcery | Model.elf | Compile c code for target
Post build tool: ssh_download.bat |  | Telnet to drone Kill Program.elf Put Model.elf Chmod Model.elf Execute Model.elf
Connect to target |  | Transfer tuneable parameters to target
Run |  | Send run command to target
Model running on AR Drone 2.0 in External mode |  |